## Slide 1
MATERIALS HANDLING &
ENGINEERING SPECIALISTS
Always moving higher

## Slide 2
Rigging, reeving and hoisting
Engineering support of power plant maintenance contractors
Various miscellaneous plant projects
MECHANICAL AND
STRUCTURAL ENGINEERING

## Slide 3
ExConTec
Real Time Analysis
Discretionary Factors
Complete Power/Tension Analysis Program

## Slide 4
Long Overland, High Lift, and High Capacity Conveyors – including horizontally curving systems, TBM trailing conveyors
High Angle Conveyors – world’s foremost authority
High Tech Transfers – association with M&J/WEBA
Plant Conveyors
Heavy Belt Feeders
Booster Drives – able to convey great lengths with modest belt strength
MATERIALS HANDLING AND
ENGINEERING SPECIALISTS
WEBA Cascade Transferring Coal at more than 9000 t/h

## Slide 5
OUR RANGE
OF SERVICES
Technical and economic studies and evaluations
New Systems
Upgrade of existing systems
Plant modifications and field advisory assistance

## Slide 6
A MOST ADVANCED
OVERLAND CONVEYOR
Quarry to Cement Plants
Pennsylvania, USA

## Slide 7
2.8 kilometer overland conveyor for an Eastern USA Cement Company
May be the world’s most advanced single flight conveyor system by virtue of the number of simultaneous advanced features, including:
Two way conveying, carrying crushed limestone, on the upper belt strand, and clinker on the return belt strand
Horizontally and vertically curving path featuring 9 horizontal curves, each with compound vertical curves
Belt turnovers, to utilize the thicker belt cover at the carrying side in either travel direction
Complete speed control with AC motors by variable frequency drives
Tripper type “Smart” booster (intermediate) drive at the upper belt strand
Tripper type “Natural” booster drive at the return strand
Multiple discharge points along the return strand
2.8 KILOMETER, TWO-WAY OVERLAND CONVEYOR

## Slide 8
2.8 KILOMETER, TWO-WAY OVERLAND CONVEYOR
ExConTec Analysis quickly reveals the tension and power distribution due to various material flow conditions

## Slide 10
DOWN HILL
CONVEYING
Gold Mine to Leaching Pads
Mezacala, Mexico

## Slide 11
OVERLAND CONVEYOR SYSTEM

## Slide 12
TB26 TAIL LOADING
TB26 HEAD DRIVE, DISCHARGE
TB27 TAIL DRIVE, LOADING
TB28 TAIL DRIVE,
TAKE-UP, LOADING
TB27 HEAD DISCHARGE

## Slide 13
History
The Technology
Installations
SANDWICH BELT HIGH ANGLE CONVEYORS

## Slide 14
PRODUCT OF EVOLUTION
FROM RESEARCH TO REALITY

## Slide 15
COVER BELTS OF THE 1950s
RUBBER TYRES PRESS COVER BELT ONTO MATERIAL

## Slide 16
COVER BELTS OF THE 1950s
 = Conveying Angle
m = Coefficient of friction for bulk material on bulk material
b = Coefficient of friction for bulk material on belt
N = Normal lineal hugging load exerted by the top belt
Wm = Lineal weight of bulk material
SANDWICH BELT MODEL #1

## Slide 17
LOOP BELTS OF THE 1970s
First use of radial pressure due to tension

## Slide 18
DOS SANTOS
SANDWICH
BELTS OF THE
1980s
A Sandwich Belt High Angle Conveyor, rationalized in the Conventional Conveyor Technology, will have the operating characteristics of a conventional conveyor:
High reliability and availability
Low operating and maintenance
THE PROPHECY

## Slide 19
S-SHAPE SANDWICH CONVEYOR
SCHEMATIC

## Slide 20
SNAKE SANDWICH CONVEYOR
SCHEMATIC
First disclosure of Snake Sandwich High Angle Conveyor

## Slide 21
MECHANICALLY PRESSED SANDWICH CONVEYOR
First disclosure of Mechanically Pressed Sandwich High Angle Conveyor

## Slide 22
STEEL CORD BELT SOLUTION
MECHANICALLY PRESSED SANDWICH CONVEYOR

## Slide 23
BASIC PROFILES
EXTENDED PROFILES
SNAKE
GPS

## Slide 24
THE ADDER SNAKE

## Slide 25
THE ADDER SNAKE

## Slide 26
CONTINUITY OF HUGGING PRINCIPLE
Material Hugging Pressure must be continuous and uniform. It must hug all of the material always, without lapse even at the smallest scale.
Radial pressure due to belt tension is the ideal and natural way to apply hugging pressure.
Applied pressure through pressing rolls must continuously distribute the pressing load by close spacing and full equalization. Such is the GPS.
CONTINUOUS & UNIFORM
RADIAL PRESSURE
PRESSURE THROUGH PRESSING ROLLS

## Slide 27
2
3
5
6
8
Sample Profile
and Details
SANDWICH BELT HIGH ANGLE CONVEYOR
4
1
7

## Slide 28
2
3
5
6
8
1
4
1. Loading onto bottom belt between skirts
7

## Slide 29
1
3
5
6
8
2
4
7
2. Top belt joins bottom belt to sandwich material

## Slide 30
3. Curve 1, bottom belt hugs material against top belt
1
2
5
6
8
3
4
7

## Slide 31
4. Inflection 1 between curves 1 and 2
1
2
5
6
8
4
3
7

## Slide 32
5. Inflection 2 between curves 2 and 3
1
2
4
6
8
5
3
7

## Slide 33
6. Inflection 3 between curves 3 and 4
1
2
4
5
8
6
3
7

## Slide 34
7. Top belt departs from curve 4 to its head/drive pulley
1
2
4
5
8
7
3
8

## Slide 35
8. Material discharge at head pulley
1
2
4
5
7
8
3
8

## Slide 36
SANDWICH BELT HIGH ANGLE CONVEYORS
General: Sandwich Belt High Angle Conveyors use all conventional conveyor equipment including smooth surfaced rubber belts that can be continuously scraped clean. They feature the operating characteristics of conventional conveyors; high reliability, low O&M costs
Capacity: Unlimited, with wide belts at typical belt speeds rates can exceed 10000 t/h
Material Size: Large belts can handle large lumps, 300mm +
Belt Speed: Recommended belt speeds are same as conventional conveyors and may exceed 5m/s in some industries
Belt Width: Unlimited, belt width is available to 3000mm wide and beyond
Important Features:

## Slide 37
Can they handle very high conveying rates?
Are they suitable for continuous operation 24/7?
Can they handle large, heavy, primary crushed ore and waste rock?
THE MOST COMMON CONCERNS
Are Sandwich High Angle Conveyors suitable for in-pit mining applications?

## Slide 38
LARGE BELTS CAN HANDLE LARGE LUMPS
SMALL BELTS HANDLE SMALL LUMPS

## Slide 39
SELECT APPLICATIONS
AT MINES AND FACILITIES

## Slide 40
Sandwich Conveyor
for
Copper Mine, Eastern Europe
Material - Copper Ore
- Density - 2.08 t/cu-m (130 PCF)
- Size - To 250 mm (10”) minus
Conveying Rate - 4000 t/h (4409 STPH)
Conveying Angle - 35.5 degrees
Belt Width - 2000 mm (78.7”)
Belt Speed - 2.85 m/s (561 FPM)
Lift - 93,500 mm (307’)
Drives
- Top Belt - 450 kW (600 HP)
- Bottom Belt - 2x450=900 kW (1200 HP)
Sandwich Conveyor
for
Gold Mine, Western USA
Material - Gold Ore
- Density - 1.6 t/cu-m (100 PCF)
- Size - 250 mm (10”) minus
Conveying Rate - 689 t/h (760 STPH)
Conveying Angle - 50 degrees
Belt Width - 1219 mm (48”)
Belt Speed - 1.65 m/s (325 FPM)
Lift - 28,900 mm (95’)
Length - 58,400 mm (191.5’)
Drives
- Top Belt - 37.3 kW (50 HP)
- Bottom Belt - 56 kW (75 HP)
DSI Snake Sandwich Conveyor
for
Empire Iron Ore Mining Partnership
Material - Iron Ore
- Density - 2.4 t/cu-m (150 PCF)
- Size - 2 mm (.08”) minus
Conveying Rate - 793 t/h (780 LTPH)
Conveying Angle - 65 degrees
Belt Width - 1067 mm (42”)
Belt Speed - 2.29 m/s (450 FPM)
Lift - 11,522 mm (37.8’)
Length - 21,489 mm (70.5’)
Snake Drives
- Top Belt - 29.8 kW (40 HP)
- Bottom Belt - 37.3 kW (50 HP)
DS 91
DS 92
SNAKE CONVS. ELEVATION
DSI Snake #2 Sandwich Conveyor
for
Continental CN at Snap Lake Diamond Mine
(Initial / Future)
Material - Kimberlite
- Density - 1.6 t/cu-m (100 PCF)
- Size - 50 mm (2”) minus
Conveying Rate - 250/500 t/h (276/552 STPH)
Conveying Angle - 49.5 degrees
Belt Width - 914 mm (36”)
Belt Speed - 1.5/2.2 m/s (295/433 FPM)
Lift - 18,310 mm (60.1’)
Length - 70,562 mm (231.5’)
Snake Drives
- Top Belt - 22.4/44.8 kW (30/60 HP)
- Bottom Belt - 22.4/44.8 kW (30/60 HP)
DSI Snake #1 Sandwich Conveyor
for
Continental CN at Snap Lake Diamond Mine
(Initial / Future)
Material - Kimberlite
- Density - 1.6 t/cu-m (100 PCF)
- Size - 32 mm (1.3”) minus
Conveying Rate - 275/550 t/h (303/606 STPH)
Conveying Angle - 49.5 degrees
Belt Width - 914 mm (36”)
Belt Speed - 1.5/2.2 m/s (295/433 FPM)
Lift - 18,310 mm (60.1’)
Length - 39,015 mm (128’)
Snake Drives
- Top Belt - 22.4/44.8 kW (30/60 HP)
- Bottom Belt - 22.4/44.8 kW (30/60 HP)
DSI Snake #1 Sandwich Conveyor
for
Victor Diamond Mine Project
Material - Kimberlite
- Density - 1.6 t/cu-m (100 PCF)
- Size - 28 mm (1.1”) minus
Conveying Rate - 381 t/h (420 STPH)
Conveying Angle - 49.5 degrees
Belt Width - 1067 mm (42”)
Belt Speed - 2 m/s (394 FPM)
Lift - 18,508 mm (60.7’)
Length - 67,581 mm (221.7’)
Snake Drives
- Top Belt - 29.83 kW (40 HP)
- Bottom Belt - 29.83 kW (40 HP)
DSI Snake #2 Sandwich Conveyor
for
Victor Diamond Mine Project
Material - Kimberlite
- Density - 1.6 t/cu-m (100 PCF)
- Size - 6 mm (1/4”) minus
Conveying Rate - 185 t/h (204 STPH)
Conveying Angle - 49.5 degrees
Belt Width - 1067 mm (42”)
Belt Speed - 1.0 m/s (197 FPM)
Lift - 18,508 mm (60.7’)
Length - 65,981 mm (216.5’)
Snake Drives
- Top Belt - 18.65 kW (25 HP)
- Bottom Belt - 18.65 kW (25 HP)
DSI Snake #3 Sandwich Conveyor
for
Victor Diamond Mine Project
Material - Kimberlite
- Density - 1.6 t/cu-m (100 PCF)
- Size - 28 mm (1.1”) minus
Conveying Rate - 422 t/h (465 STPH)
Conveying Angle - 60 degrees
Belt Width - 1067 mm (42”)
Belt Speed - 2 m/s (394 FPM)
Lift - 11,886 mm (39.0’)
Length - 33,282 mm (109.2’)
Snake Drives
- Top Belt - 29.83 kW (40 HP)
- Bottom Belt - 29.83 kW (40 HP)
DS 012
Sandwich Conveyor
for
Coal Prep Plant, Eastern USA
Material - Refuse
- Density - 1.28 t/cu-m (80 PCF)
- Size - 135 mm (5.3”) minus
Conveying Rate - 454 t/h (500 STPH)
Conveying Angle - To 41 degrees
Belt Width - 914 mm (36”)
Belt Speed - 2.34 m/s (460 FPM)
Lift - 174,800 mm (574’)
Length - 454,200 mm (1490’)
Drives
- Top Belt - 186.5 kW (250 HP)
- Bottom Belt - 186.5 kW (250 HP)
Downhill Sandwich Conveyor
from
Phosphate Mine, Venezuela
Material - Phosphate Rock
- Density - 1.60 t/cu-m (100 PCF)
- Size - 6.3 mm (1/4”) minus
Conveying Rate - 668 t/h (736 STPH)
Conveying Angle - 35.5 degrees
Belt Width - 914 mm (36”)
Belt Speed - 2.29 m/s (450 FPM)
Elevation Drop - 34,000 mm (111.5’)
Length - 113,000 mm (371’)
Drive
- Bottom Belt - 93.2 kW (125 HP)

## Slide 41
Precluded tripling of the truck fleet (eliminated 10 trucks)
Precluded the need for 4 km of haulage ramps, 3.5 km of which would be of constant ascent
Savings of US $12 million per year (TODAY $22 million)
THE MAJDANPEK IPCC SYSTEM
FIRST FIVE YEARS PERFORMANCE
1992-1997

## Slide 42
Majdanpek IPCC System, Serbia
Sandwich Conveyor
for
Copper Mine, Eastern Europe
Material - Copper Ore
- Density - 2.08 t/cu-m (130 PCF)
- Size - To 250 mm (10”) minus
Conveying Rate - 4000 t/h (4409 STPH)
Conveying Angle - 35.5 degrees
Belt Width - 2000 mm (78.7”)
Belt Speed - 2.85 m/s (561 FPM)
Lift - 93,500 mm (307’)
Drives
- Top Belt - 450 kW (600 HP)
- Bottom Belt - 2x450=900 kW (1200 HP)

## Slide 43
UHAC -Vital Link for IPCC System Western Australia

## Slide 44
Snake Sandwich Conveyor
for
UBT, Davant, LA, USA
Material - Coal
- Density - 0.80 t/cu-m (50 PCF)
- Size - 76 mm (3”) minus
Conveying Rate - 3629 t/h (4000 STPH)
Conveying Angle - 52 degrees
Belt Width - 2438 mm (96”)
Belt Speed - 4.32 m/s (850 FPM)
Lift - 18,540 mm (60.8’)
Length - 45,900 mm (150.6’)
Snake Drives
-Top Belt - 224 kW (300 HP)
- Bottom Belt - 224 kW (300 HP)
SNAKE CONV. ELEV.
SNAKE CONV. PLAN
WIDEST BELTS AND HIGHEST VOLUMETRIC RATE
UNITED BULK TERMINAL
DAVANT, LOUISIANA USA

## Slide 45
A PICTURE IS WORTH A THOUSAND WORDS
HOW VERSATILE ARE SANDWICH BELT HIGH ANGLE CONVEYORS

## Slide 46
SUMMARY
WIDE APPLICATIONS
Mines and quarries
Plants and marine terminals
Pulp and paper mills
Etc
The Dos Santos Sandwich Belt Conveyor uses all conventional conveyor components and equipment and features
Unlimited capacity
Characteristics of conventional conveyors
  Efficiency
  Reliability
  Cost effectiveness
Sandwich Belt conveyors are proven and technologically mature
SANDWICH CONVEYORS

## Slide 47
SANDWICH BELT HIGH ANGLE CONVEYOR SYSTEM STUDY
GOLD COPPER MINE
EUROPE

## Slide 48
Primary ore crusher at lower left conveyor system leading to the processing plant at the upper left
DEVELOPED MINE PIT

## Slide 49
ORE CONVEYING PLAN
Material | Copper, Gold Ore
Bulk Density | 1.75 t/cu-m
Size | 250mm minus
Design Rate: | 1870 t/h
Design Parameters

## Slide 50
COMPLETE SYSTEM
Sacrificial Conveyor
High Angle Stacker
Main High Angle Conveyor

## Slide 51
THANK YOU!
ANY QUESTIONS?